## Slide 1: Copper Mining and Processing

## Slide 2: Learning Objectives
Describe basic information about copper, its occurrence, and its use
Articulate the history and current status of copper mining in Arizona and tribal lands
Detail the stages in the life cycle of a mine
Describe copper processing for oxide and sulfide ores

## Slide 3: Copper, its Occurrence, and Use
What is Copper?

## Slide 4: What is Copper?
Reddish-orange bright metallic luster
Found as native (pure) copper or combined with other elements
Ductile and malleable
Good conductor of heat and electricity
Resistant to corrosion
Can be alloyed to make bronze and brass
Copper
29
Cu
63.54

## Slide 5: Copper, its Occurrence, and Use
Naturally Occurring Forms of Copper

## Slide 6: Forms of Copper
Native (pure) copper
Copper sulfides (e.g. chalcopyrite and chalcocite)
Copper oxides (e.g. cuprite)
Copper carbonates (e.g. azurite and malachite)
Azurite
Cuprite
Chalcopyrite
Malachite
Chalcocite
Notes: Copper sulfide and oxide ores are the forms most commonly mined for copper

## Slide 7: Copper Ores
Copper ores are complex
  Can contain metals, other elements, and non-metallic minerals
In the ore, copper is less than 1%
Depending on the ore, it requires different mining and extraction processes to yield 99.99% pure copper

## Slide 8: Copper, its Occurrence, and Use
Historical and Modern Copper Use

## Slide 9: Historical Copper Use
Discovered: early 9000 BC in Middle East
Early artifacts used native (pure) copper
  Utensils, tools, weapons, piping, ornaments, and jewelry
Chalcolithic period: ~3500-2500 BC
  Rise in the use and smelting of copper
  Discovery of bronze alloy
  Early Romans discovered brass alloy
  Copper and brass as currency

## Slide 10: Historical Copper Use in the US
  Largest deposit of native copper found in Michigan at Keweenaw mines
  Native Americans mined copper~5000–1200 BC
  Found as knives, arrows, spear heads, and axes throughout Americas
  Copper not mined on a commercial scale until 1840s

## Slide 11: Copper in our Modern Lives
Common copper alloys are bronze and brass
Currency
Cooking pots
Wiring/Electronics
Jewelry
Notes: bronze (e.g., statues) and brass (e.g., French horn)

## Slide 12: Major Modern Copper Uses
Copper consumption by major U.S. markets in 2013. Source: Copper Development Association Inc. Annual Data (2014).

## Slide 13: World Consumption of Copper
Worldwide consumption of copper has increased greatly over the past century
Leading consumers1:
  Asia
  Europe
  The Americas
Leading producers2 (tons/year):
  Chile (5.7 million)
  China (1.7 million)
  Peru (1.3 million)
  US (1.2 million)
  Australia (1 million)
Source: 1 IWCC, 2013; 2 USGS, 2014

## Slide 14: US Copper Production
In the United States, approximately 99% of the $9 billion dollars’ worth of copper produced comes from five states: Arizona, Utah, New Mexico, Nevada, and Montana
ARIZONA
UTAH
NEW MEXICO
NEVADA
MONTANA
Source: USGS, 2014

## Slide 15: Copper Mining in Arizona
Arizona Copper Production

## Slide 16: Arizona: The “Five C’s”
Cattle
Cotton
Citrus
Climate
Copper

## Slide 17: Copper and the Arizona Economy
Arizona produces approximately 65% of the country’s copper1
In 2011, copper mining contributed2:
  $4.6 billion direct and indirect economic benefits
  49,800 jobs
  Arizona is home to the Morenci Mine which is one of the largest in the world3
Source: 1 USGS, 2014; 2 AZ Mining Assoc., 2011; 3 Freeport-McMoRan, 2014

## Slide 18
Arizona Major Mines in 2014
Adapted from Arizona Geological Survey Map 38 by Nyal Niemuth

## Slide 19: Copper Mining in Arizona
Environmental Regulation

## Slide 20: Environmental Regulation
Regulatory agencies ensure that mines do not release hazardous materials outside of mine site
  US Environmental Protection Agency
  AZ Department of Environmental Quality
  County Department of Environmental Quality
  Tribal Environmental Protection Agency
  Mining companies have personnel in place to interact with the regulatory agencies

## Slide 21: Copper Mining on Tribal Lands
Arizona

## Slide 22: Mining on Tribal Lands
Twenty-one federally-recognized tribes own lands that cover 19.7 million of Arizona’s 72.9 million acres, or 27% of the state
"Canyon de Chelly, Navajo" by Edward S. Curtis - REPOSITORY: Library of Congress Prints and Photographs Division. Public Domain via Wikimedia Commons.

## Slide 23
Major Mines and Tribal Lands

## Slide 24: Copper Mining on Tribal Lands
Tohono O’odham Nation

## Slide 25: Tohono O’odham Nation
Owns 2.7 million acres, or 3.7% of the state
Metallic minerals mined throughout history:
  Copper, gold, silver, lead, zinc, iron, mercury, manganese, uranium, and tungsten
Within Pima County portion of the Nation:
  ~210 metallic mineral deposits, mines, prospects, and quarries
  Many smaller mines are results of small-time prospectors and now abandoned
Mission Cu Mine

## Slide 26: Copper Mining on Tribal Lands
Case Study #1: Mission Mine

## Slide 27: Mission Mine
19,000 acre mine located on the south end of San Xavier District
Current pit:
  2.5 miles long
  1.5 mile wide
  1,200 feet deep

## Slide 28: Mission Mine
In 2012:
  Produced 134 million pounds of copper concentrate
  Paid $6.6 million in state royalties and $2.5 million in tribal royalties
  Employed 620 people
Expected to produce until 2033

## Slide 29: Mission Mine
Violations for dust emissions and water discharges
Works with regulatory agencies to achieve compliance

## Slide 30: Copper Mining on Tribal Lands
Case Study #2: Cyprus Tohono Mine

## Slide 31: Cyprus Tohono Mine
4,180 acre mine located in the Sif Oidak District
Currently in care and maintenance mode, but may resume operations

## Slide 32: Cyprus Tohono Mine
Listed as a Superfund Alternative site in 2009
  Groundwater contaminated with uranium, sulfate, and perchlorate
Agency for Toxic Substances and Disease Registry has completed a Health Consultation

## Slide 33: Tribal Concerns with Mining

## Slide 34: Tribal Concerns
Tribes have faced displacement, discrimination, and marginalization due to mining
Mining can be a source of contamination that impacts the health of neighboring communities and the environment

## Slide 35: Tribal Concerns
Concerns may include:
  Poor air quality
  Contaminated water
  Occupational hazards which can be a result of direct exposure to dust during metal/mineral extraction
Enforcement of mine safety issues is regulated by the Mine Safety and Health Administration, a division of the US Department of Labor

## Slide 36: Tribal Concerns
Mining can have impacts on sacred lands and artifacts as well as natural resources
  On the Navajo Nation people used uranium mill tailings to build their traditional earthen homes (hogan), many of which remain in use today
  100 sacred and cultural sites of the Tohono O’odham Nation may be impacted by the proposed Rosemont Copper Mine
  Lands sacred to the San Carlos Apache may be impacted by the proposed Resolution Copper Mine

## Slide 37: Life Cycle of a Mine

## Slide 38: Life Cycle of a Mine
Prospecting/Exploration: Finding and defining it
Development:
Planning and building it
Extraction:
Mining it
Closure/Reclamation: Cleaning it up
Prospecting/ Exploration
Development
Extraction
Closure/ Reclamation

## Slide 39: Life Cycle of a Mine
Prospecting/Exploration (Finding and Defining it)
Prospecting/ Exploration

## Slide 40: Prospecting/Exploration
Precursor to mining
Overlapping stages
~2-8 years total
~$500K-$15 million total
"Prospector George Warren" by Unknown, published by S.J. Clarke Publishing Company (1916). Public Domain via Wikimedia Commons.
George Warren, American prospector in Bisbee, Arizona, who discovered the Queen Creek copper deposits.

## Slide 41: Prospecting
Geologic mapping
  Geophysics
  Geochemistry
  Drilling
  Photography and mapping
  May or may not lead to discovery of valuable minerals

## Slide 42: Exploration
Acquire mineral rights lease as needed
Additional techniques more accurately determine size and value of mineral deposit:
  Is it a mineral resource or ore reserve?
  Allows estimate of how much it is worth + how much will it cost to mine it
Notes: .

## Slide 43: Mineral Resource
Concentrated, potentially valuable material that can be mined for economic profit
Whether it is worth mining may depend on:
  Amount, form, location, and quality of the material (i.e., geological confidence)
Source: JORC, 2012

## Slide 44: Mineral Resource
Geological methods classify a mineral resource according to geological confidence:
  Inferred
    Limited sampling, low confidence ore is there
  Indicated
    More sampling, some confidence ore is there, but still just an estimate
  Measured
    More sampling, high confidence ore is there and that estimate is accurate
Source: JORC, 2012

## Slide 45: Ore Reserve
The part of the mineral resource that can be economically profitable to mine
  I.e., there is enough valuable metal to be worth extracting it from the surrounding rock
Source: JORC, 2012

## Slide 46: Ore Reserve
Classified based on what is known about the mineral resource + “modifying factors”
  Factors include mining, metallurgic, economic, environmental, marketing, legal, political, and social considerations
  Probable
    Some confidence ore is there, some uncertainty in modifying factors  mine could be successful, but there is still some risk
  Proved
    High confidence ore is there, little uncertainty in modifying factors  mine is likely to be economically succesful
Source: JORC, 2012

## Slide 47: General relationship between Mineral Resources and Ore Reserves
Inferred
Limited sampling,
low confidence about what’s really there
Indicated
More sampling,
more confidence,
but still an estimate
Probable
Some confidence in ore + some uncertainty in modifying factors
Measured
Additional sampling, high confidence estimate is accurate
Proved
High confidence in ore
+ little uncertainty in modifying factors
  Increasing Economic Favorability
  Increasing geological sampling/confidence
Exploration Results
Mineral Resource
(classified on geological confidence)
Ore Reserve
(classified on geological confidence + certainty of modifying factors)
Based on analysis of “modifying factors” including mining, metallurgic, economic, environmental, marketing, legal, political, and social considerations
Adapted from: Australasian Code for Reporting of Exploration Results, Mineral Resources and Ore Reserves. Source: JORC, 2012

## Slide 48: Exploration
Final step: produce a feasibility report
  How much is the ore worth?
  How much will it cost to mine it?
  Bottom line: Is it a good investment to open this mine?
Mining organization can now make a decision about whether the project will be abandoned or continued…
Notes: .

## Slide 49: Life Cycle of a Mine
Development (Planning and Building it)
Development

## Slide 50: Development
~4-12 years total
~$1 million - $1 billion
Extensive logistical planning and paperwork:
  Budget and financial reports prepared
  Permits requested
  Environmental and community impacts assessed

## Slide 51: Development
  Which mining process/ technology will be used
    Surface, underground, solution
  Building of access roads
  Identification of resources
    e.g., power and water sources
  Construction of ore processing facilities and disposal areas for waste
Plans for infrastructure are assessed:

## Slide 52: Development
Mine site is developed just enough to ensure it can be productive for the life cycle of the mine, without later interruption
By this stage, ~$10s of millions - $100s of millions may have been invested in the project
  …But it may fail to open if the pre-development requirements are not met, including acceptance by the community!

## Slide 53: Life Cycle of a Mine
Extraction (Mining it)
Extraction

## Slide 54: Extraction
  The mine begins producing, removing the mineral from earth in large quantities
    This is typically what we picture when we think of mining
"Morenci Mine 2012" by Stephanie Salisbury - IMG_4218. Licensed under CC BY 2.0 via Commons - https://commons.wikimedia.org/wiki/File:Morenci_Mine_2012.jpg#/media/File:Morenci_Mine_2012.jpg

## Slide 55: Extraction
Typically ~5-30 years total
  But many mines are now open for 100+ years
Can cost ~$several million - $100s of millions per year
  Depends on size of mine, location, etc.

## Slide 56: Life Cycle of a Mine
Closure/Reclamation (Cleaning it up)
Closure/ Reclamation

## Slide 57: Closure/Reclamation
~1-5 years for closure and up to 35 years or more for reclamation
Can cost $millions - $100s of millions depending on many factors
  E.g., age, location, type, and size of mine, amount of waste, geological characteristics, and type of mineral

## Slide 58: Closure/Reclamation
Planning for mine closure and reclamation begins early on:
  The mine is not allowed to open without a plan for closure in place already
  Federal and state regulations require mining companies to post funding for closure prior to the mining project beginning

## Slide 59
Closure considerations include:
  Protecting public health and safety
  Addressing environmental damage
  Returning land to its original or accepted state
  Sustaining social and economic benefits brought by mine
Closure

## Slide 60
Reclamation plans describe the processes that will attempt to restore or redevelop the land that has been mined to a more natural or economically usable state
Reclamation

## Slide 61: Processing of Copper Ores

## Slide 62: Processing of Copper Ores
The copper ores undergo different processing depending on their chemistries
Oxide Ore: Hydrometallurgy
Heap Leaching
Solvent Extraction
Electrowinning
Mining
Transporting
Primary Crushing
Sulfide Ore: Pyrometallurgy
Froth Floatation
Thickening
Smelting
Electrolysis
Final Product:
99.99% pure copper cathode

## Slide 63: Mining and Transporting

## Slide 64: Primary Crusher
The primary crusher reduces the size of the ore from boulder to golf ball-sized rocks

## Slide 65: Processing of Oxide Ore
(For example, Cyprus Tohono Mine)

## Slide 66: Processing Copper Oxide Ore
Oxide ores are generally processed using hydrometallurgy
Mining considerations:
  Oxide ore is usually lower-grade (contains less copper)
  Oxide ore is often more abundant near the surface
  Hydrometallurgy process is less expensive

## Slide 67: Hydrometallurgy
Uses aqueous (water-based) solutions to extract and purify copper from copper oxide ores, usually in three steps:
  Heap leaching
  Solvent extraction
  Electrowinning

## Slide 68: Heap Leaching
Uses percolating chemical
solutions to leach out
metals from the ore
Commonly used for low-
grade ore
Process consists of:
  Crushed ore is piled into a heap on a slope (impenetrable layer)
  Leaching reagent (dilute sulfuric acid) is sprayed and trickles though heap to dissolve copper from the ore
  Pregnant leach solution and copper sulfate is collected in a small pool
  Copper compound contains between 60-70% copper

## Slide 69: Solvent Extraction
Two immiscible (un-mixing) liquids are stirred and allowed to separate, causing the copper to move from one liquid to the other
  Pregnant leach solution is mixed with a solvent
  Copper moves from the leach solution into the solvent
  Liquids separate based on
  solubility
    Copper remains in solvent
    Impurities remain in the leach
    solution (which is recycled)

## Slide 70: Heap Leaching and Solvent Extraction

## Slide 71: Electrowinning
Electrical current passes through an inert anode (positive electrode) and through the copper solution from the previous step, which acts as an electrolyte
Positively-charged copper ions (called cations) come out of solution and are plated onto a cathode (negative electrode) as ~99.99% pure copper
Electrowinning, Inspiration Consolidated Copper Co., Globe AZ. By Keyes, Cornelius M. 1972. U.S. National Archives and Records Administration. Public domain via Wikimedia Commons.

## Slide 72: Electrowinning

## Slide 73: Processing of Sulfide Ore
(For example, Mission Mine)

## Slide 74: Processing Copper Sulfide Ore
Sulfide ores are generally processed using pyrometallurgy
Mining considerations:
  Sulfide ore is often less abundant
  Pyrometallurgy process is more expensive
  Sulfide ore is often a higher-grade ore (contains more copper)
  Ultimately more copper can be extracted from sulfide ore deposits

## Slide 75: Pyrometallurgy
Uses physical steps and high temperatures to extract and purify copper from copper sulfide ores, usually in four steps:
  Froth flotation
  Thickening
  Smelting
  Electrolysis
Hot slag pours from smelter of Inspiration Consolidated Copper Company” by Keyes, Cornelius M. 1972. U.S. National Archives and Records Administration. Public Domain via Wikimedia Commons.

## Slide 76: Froth Flotation
Crushed ore is further processed at a mill to fine sand
Liquid is added to make a slurry (copper ore and gangue)
Chemical reagents are added to bind the copper and make it waterproof
"Froth flotation" by Andreslan. Public Domain via Wikimedia Commons.

## Slide 77: Froth Flotation
Air is blown into the slurry to make bubbles, which carry the waterproof copper to the top of the tank where it is skimmed off
Impurities drop to the bottom of the tank

## Slide 78: Thickening
Copper froth poured into large tanks (thickeners)
Bubbles break open, copper solids settle at the bottom
  Filtered to remove water
  Thickened copper concentrate contains metals, impurities and ~30% copper

## Slide 79: Smelting
  Copper concentrate is sent through the smelting furnace (2,300 °F)
  Converted into molten liquid
Liquid is poured into slag-settling furnace to produce:
  Matte: mixture of copper, sulfur, iron (~58-60% copper)
  Slag: dense, glassy material containing silica and other impurities

## Slide 80: Smelting
Molten matte copper is sent to the converter furnace
  Impurities are burned off
  Forms yellow blister copper (98% copper)
Molten blister copper is sent to the anode smelter
  Oxygen is burned off, forming blue-green anode copper

## Slide 81: Smelting
Molten anode copper is poured into molds called anode-casting wheels
  Cooled anode slabs are 99% pure copper
    Now copper-colored
    2 inches thick, 3 feet wide, 3.5 feet high
    Weigh 750 pounds

## Slide 82: Electrolysis
Anode slabs are hung in a large tank
  Act as positive electrodes
Thin sheets of pure copper (15 lb) are hung in between anodes
  Act as cathodes/negative electrodes
Tank is filled with electrolyte solution
  Copper sulfate and sulfuric acid

## Slide 83: Electrolysis
Electric current is applied
Positively-charged copper ions (cations) leave the anode (positive electrode)
Cations move through the electrolyte solution and are plated on the cathode (negative electrode)

## Slide 84: Electrolysis

## Slide 85: Electrolysis
Other metals and impurities also leave the anodes
  Drop to the bottom of the tank or stay in solution
  Can be collected and refined to recover other valuable metals such as silver and gold
After 14 days of electrolysis, the final products are copper cathodes
  Weigh 375 pounds
  Contain 99.99% pure copper

## Slide 86
Cathode
Tubes
Plates
Wires
The finished copper cathodes can then be made into plates, wires, tubes, and other copper products.

## Slide 87: Recycling Copper
Because copper is an element, it can be infinitely recycled
New and old copper scrap or copper alloys can be melted, re-purified, and recycled into new components
  ~50% of copper used in the copper industry was recycled
  In 2010, 770,000 metric tons of copper were recycled, at estimated value of $6 billion